## Slide 1: Strength of Materials
Notes: http://www.teachengineering.org/view_lesson.php?url=collection/cub_/lessons/cub_mechanics/cub_mechanics_lesson07.xml

## Slide 2: Design
How do engineers decide if something is a good design?
Engineers use their understanding of forces, stress, strain and material properties to create safe designs for structures, equipment and products

## Slide 3: Stress
The amount of force applied over the area of an object (computed by dividing force by area)
Where (sigma lowercase) = stress
F = Force (Newtons or lbs.)
A = Cross sectional area (
Notes: What do engineers mean when they talk about stress?
Have you ever experienced something breaking because of the "stress" you put on it?

## Slide 4: Compressive and Tensile Stresses
Compressive
  Stress that squeezes a material together
Tensile
  Stress that pulls a material apart

## Slide 5: Strain
The percent amount of elongation or compression of a material
Where (epsilon upper) = strain (percent)
L = new length (mm or in)
L0 = original length (mm or in)

## Slide 6: Elastic and Plastic Deformation
Elastic deformation
  Occurs when a material is strained (deformed), but returns to its original shape, like a rubber band
Plastic deformation
  Occurs when a material is strained (deformed) beyond its yield strength and does not return to its original shape, like silly putty

## Slide 7: Properties of Materials
Engineers use their understanding of forces, stress, strain and material properties to create safe designs
Yield strength
  The maximum amount of stress a material can take before it deforms plastically (permanently)
Ultimate tensile strength
  The maximum amount of tensile stress a material can take before breaking.
Fatigue strength
  The maximum amount of stress a material can take one million times without breaking.

## Slide 8: Bridge Building